## Slide 1: Automatic Annotation of Actigraphy Data for Sleep Disorders Diagnosis Purposes
1 Institute for Systems and Robotics, Instituto Superior Técnico, Lisbon, Portugal
2 Faculty of Electrical Engineering and Computer Science, VSB – TU Ostrava, Czech Republic
3Faculdade de Medicina da Universidade de Lisboa, Lisbon, Portugal
Alexandre Domingues1, Ondrej Adamec1,2, Teresa Paiva3 and J. Miguel Sanches1

## Slide 2: Structure
Motivation
Actigraphy
Data sets
Data classification
Results
Conclusions

## Slide 3: Motivation
Sleep disorders
Affect a significative percentage of young and adult population.
Can be related with diabetes, obesity, depression and cardiovascular diseases.
Diagnosis involves complex and intrusive procedures.
Many individuals never seek medical care.

## Slide 4: Motivation
Diagnosis
Standard procedure:
Polysomnography
Several physiological signals are acquired (EEG, EOG, EMG, Oxymetry,etc…)
Data is acquired in a controled and reliable environment

## Slide 5: Motivation
Diagnosis
PSG - Difficulties
Performed in medical facilities
The exam is highly intrusive.
Long term monitoring is not feasible
Data processing is done offline and is a time consuming process.
Faster, low cost and Portable methods are needed!

## Slide 6: Actigraphy
Non invasive and portable sensor.
Low cost solution to gather valuable information
Allows for long term monitoring.
Automatic determination of the
Sleep / Wakefulness state

## Slide 7: Data sets
Collected from 23 healthy subjects for a period of 14 days.
Segmented by trained technicians with the help of light information and a sleep diary.
Data segments grouped into two large sleep and wakefulness arrays.

## Slide 8: Statistical properties extraction
Two large arrays of Sleep/Wakefulness data
‘W’
overlapping windows
‘p’ order autoregressive model (α = parameters)
α11 … … … … … α1p
α21 … … … … … α2p
α31 … … … … … α3p
αw1 … … … … … αwp
Time

## Slide 9: Bayes classifier
Clouds of parameters of each class described by a Gaussian distribution
Each class (ws , ww) described by a pair of features:
New set of data
Bayes classifier
Classification into wakefulness or sleep state

## Slide 10: Results
Performance of the estimator
Leave-one-out Cross-validation:
Accuracy ≈ 96%
Sensitivity ≈ 98%
Specificity ≈ 74%

## Slide 11: Results
Distribution of the coefficients obtained with a 2nd order autoregressive model

## Slide 12: Results
Bayes factor for 2 days/nights

## Slide 13: Results
Detection of a wakening episode

## Slide 14: Conclusions
Classification procedure with real actigraphy data. Based on autoregressive (AR) models
Bayes classifier with 96% accuracy.
Future work
More physiological data, e.g., light, position, oximetry, and temperature.
Step toward an alternative method in the diagnosis of some sleep disorders involving long term monitoring – Light Polysonmography (LPSG)

## Slide 15
Thank You
32nd Annual International Conference of the IEEE Engineering in Medicine and Biology Society